## Slide 1
SHOP DRAWINGS — ELECTRICAL / AGL SCOPE
RECTIFICATION OF TWY E BETWEEN E4 & E6 (ZIA)
AGL WORKS AT THREE (3) MILLING LOCATIONS — FIELD CONDITION SCOPE
REV P07 — SCOPE PER FIELD SHEETS Document_3 (LOC-01) AND Second_milling_area rev _1 (LOC-02 / LOC-03)
Document No.
AUH-SK-AGL-TWYE-001
Base layer
As-built AGL asset survey assets_20260726120533.xlsx — UTM 40N (EPSG:32640)
Prepared by
Approved by
Mohammed — AGL Team Leader, ADB SAFEGATE AGL Team · Issued 28.07.2026 · Rev P07 30.07.2026
Ragesh Menon — AGL Manager, ADB SAFEGATE AGL Team

## Slide 2
SHOP DRAWING — ELECTRICAL / AGL SCOPE (FIELD-GOVERNED) · TAXIWAY E (E4–E6) — LOCATION 1 · DWG NO AUH-SK-AGL-TWYE-001-1001 REV P07
UTM 40N (EPSG:32640) — AS-BUILT POSITIONS · DO NOT SCALE FROM DRAWING
AGL WORKS DEMARCATION — PER FIELD-VERIFIED AFFECTED ASSETS (572.6 m²)
RRM.76
TCCECH.04.018
RRM.540
RRM.541
RRM.636
TCC103.12.019
TCC103.11.019
TCC103.11.020
TEC102.02.047
TEC102.02.048
TEC102.02.049
HH.E6.033
TCCECH.03.017
TCCECH.04.016
TCCECH.03.016
TCCECH.04.015
TCCECH.03.015
TCC103.11.027
TCCECH.03.038
TCCECH.04.037
TCCECH.03.039
TCCECH.04.038
TCCECH.04.019
TCCECH.03.020
X_CV_STH_PITS &.27152
X_CV_STH_PITS &.27153
X_CV_STH_PITS &.27154
X_CV_STH_PITS &.27162
HH.E6.038
HH.E6.037
HH.E6.036
HH.E6.035
HH.E6.041
HH.E6.042
HH.E6.034
HH.E6.032
HH.E6.039
P6.009
P6.038
MH.E.024
MH.E.014
X_CV_STH_PITS &.23918
SGC102.02.017
SGC102.02.016
TEC102.02.050
SBC102-02/024
SBC102-01/027
SBC102-02/025
SBC102-01/028
SBC102-02/026
SBC102-01/029
TCCECH-04/034
TCCECH-03/036
TCCECH-04/035
TCCECH-03/037
TCCECH-04/036
SBC102-02/027
TCCECH-03/035 + 03/018 (0.49 m apart)
SBC102-01/026
LOCATION 1 — 1001 · REV P07 (ISSUED)
SCOPE PER FIELD SHEET Document_3 (15 No. LIGHTS LISTED) — FIELD CONDITION GOVERNS
Sheet A3 (420 x 297 mm) · NOT TO SCALE — approx. 1:465 as plotted · UTM 40N · Issued 28.07.2026 · Rev P07 30.07.2026 · Prepared: Mohammed, AGL Team Leader — ADB SAFEGATE · Approved: Ragesh Menon, AGL Manager
SCOPE / QUANTITIES (PER FIELD VERIFICATION)
CORE OUT SHALLOW BASE + NEW CABLE: 11 No. (SEC. CABLE YES / SHALLOW BASE YES)
• VIA DUCT (6): SBC102-02/024, 01/027, 02/025, 01/028, 02/026, 01/029
• VIA SAWCUT (5): TCCECH-04/034, 03/036, 04/035, 03/037, 04/036
NEW SECONDARY CABLE ONLY — NO CORING: 3 No. (SEC. CABLE YES / SHALLOW BASE NO)
• VIA DUCT (1): SBC102-02/027
• VIA SAWCUT (2): TCCECH-03/035, 03/018 — 0.49 m apart, one shared label; bases sound, verify at cut line
FIELD VERIFIED NOT AFFECTED: SBC102-01/026 (SEC. CABLE NO / SHALLOW BASE NO — no works)
FIELD SHEET TOTAL: 15 No. — 14 secondary cables, 11 core-outs, 0 dummy plates
NOT ON FIELD SHEET — CONFIRM BEFORE WORKS: TCC103-11/021, 11/126, 12/021, 12/022
• secondary routes appear to cross the cut; not listed on Document_3 — shown grey, no action assumed
ISOLATE CIRCUITS: SBC102.01/.02, TCCECH.03/.04
SITE RECORD 23.07.2026: 9 cored + 2 reinstatement completed
GENERAL NOTES
1. All asset positions as-built (asset survey assets_20260726120533.xlsx, UTM 40N / EPSG:32640).
2. AGL works demarcation (red) drawn around field-verified affected assets (+2.0 m) — field condition governs.
3. Secondary cables: no joints — full manhole-to-light replacement. Confirm routes vs AGL duct-layout CAD (Rev C) before works.
4. Isolate, lock out & prove dead all listed circuits at CCR under permit before any cutting, coring or excavation.
5. Reinstatement setting-out by civil survey from as-built E/N, checked against adjacent undisturbed fittings before coring.
6. Rev P07: every asset on this sheet re-marked directly from field sheet Document_3 — outer ring from the Secondary-cable / Shallow-base columns, inner disc from Duct / Sawcut. Assets not listed on the field sheet are shown grey with no action assumed.
7. Asset key: label prefix to as-built class, from the AGL asset survey checked against the AGL duct-layout CAD. Civil items (HH / MH / pits / RRM) plot about 2.1 m from the surveyed insertion point — set out from survey, not from this sheet. A pit prefix can cover more than one civil class (manhole, transformer handhole, earthing); confirm the individual pit before works.
TCC103-11/021
TCC103-11/126
TCC103-12/021
TCC103-12/022
WORKS ACTIONS
CORE OUT + NEW CABLE (DUCT)
CORE OUT + NEW CABLE (SAWCUT)
NEW SEC. CABLE ONLY (DUCT)
NEW SEC. CABLE ONLY (SAWCUT)
NOT AFFECTED / NOT ON FIELD SHEET
EXISTING ASSETS (AS-BUILT)
EXISTING AGL ASSET — see asset key
AGL FEED MANHOLE / HANDHOLE
AREAS & LINEWORK
MILLING / CUT AREA
AGL WORKS DEMARCATION (GOVERNING)
SECONDARY DUCT CROSSING CUT (INDIC.)
INDICATIVE DUCT — LIGHT TO MH / HH
TAXIWAY CENTRELINE (THROUGH TCC)
STOP BAR (THROUGH SBC)
TWY EDGE / PAVEMENT (INDIC. 23 m)
ASSET KEY (AS-BUILT LABEL PREFIX)
SBC102 — Stop bar light ×8
SGC102 — Sign foundation ×2
TCC103 — Taxiway centreline light ×8
TCCECH — Taxiway centreline light ×17
TEC102 — Taxiway edge light ×4
HH — Handhole ×10
MH — Manhole ×2
P6 — Civil pit (manhole / earthing point) ×2
RRM — Runway guard light / RRM ×4
X_CV_STH_PITS — Civil pit / transformer HH ×5

## Slide 3
SHOP DRAWING — ELECTRICAL / AGL SCOPE (FIELD-GOVERNED) · TAXIWAY E (E4–E6) — LOCATION 2 · DWG NO AUH-SK-AGL-TWYE-001-1002 REV P07
UTM 40N (EPSG:32640) — AS-BUILT POSITIONS · DO NOT SCALE FROM DRAWING
AGL WORKS DEMARCATION — PER FIELD-VERIFIED AFFECTED ASSETS (700.3 m²)
RRM.545
RRM.546
RRM.554
RRM.556
X_CV_STH_PITS &.24043
TCCECH.03.010
TCCECH.04.009
TCCECH.04.006
TCCECH.03.006
P2.002
HH.E.055
HH.E.056
TCCECH-03/007
TCCECH-04/007
TCCECH-03/008
TCCECH-04/008
TCCECH-03/009
RRM.555
LOCATION 2 — 1002 · REV P07 (ISSUED)
SCOPE PER FIELD SHEET Second_milling_area rev _1 (5 No. LIGHTS LISTED) — FIELD CONDITION GOVERNS
Sheet A3 (420 x 297 mm) · NOT TO SCALE — approx. 1:465 as plotted · UTM 40N · Issued 28.07.2026 · Rev P07 30.07.2026 · Prepared: Mohammed, AGL Team Leader — ADB SAFEGATE · Approved: Ragesh Menon, AGL Manager
SCOPE / QUANTITIES (PER FIELD VERIFICATION)
NEW SECONDARY CABLE ONLY (VIA DUCT): 5 No.
• TCCECH-03/007, 04/007, 03/008, 04/008, 03/009
NO SHALLOW BASES AFFECTED — COLUMN BLANK ON FIELD SHEET, CONFIRMED ‘NO’ 30.07.2026; NO ASSET LIES INSIDE THE MILLING POLYGON
RRM.555 (0.41 m from cut): REMOVE / PROTECT BEFORE SAWCUT, RE-FIX AFTER PAVING
ISOLATE CIRCUITS: TCCECH.03, TCCECH.04
GENERAL NOTES
1. All asset positions as-built (asset survey assets_20260726120533.xlsx, UTM 40N / EPSG:32640).
2. AGL works demarcation (red) drawn around field-verified affected assets (+2.0 m) — field condition governs.
3. Secondary cables: no joints — full manhole-to-light replacement. Confirm routes vs AGL duct-layout CAD (Rev C) before works.
4. Isolate, lock out & prove dead all listed circuits at CCR under permit before any cutting, coring or excavation.
5. Reinstatement setting-out by civil survey from as-built E/N, checked against adjacent undisturbed fittings before coring.
6. Rev P07: every asset on this sheet re-marked directly from field sheet Second_milling_area rev _1 (2nd table) — outer ring from the Secondary-cable / Shallow-base columns, inner disc from Duct / Sawcut. Assets not listed on the field sheet are shown grey with no action assumed. Shallow-base column blank on that sheet; confirmed ‘NO’ 30.07.2026.
7. Asset key: label prefix to as-built class, from the AGL asset survey checked against the AGL duct-layout CAD. Civil items (HH / MH / pits / RRM) plot about 2.1 m from the surveyed insertion point — set out from survey, not from this sheet. A pit prefix can cover more than one civil class (manhole, transformer handhole, earthing); confirm the individual pit before works.
WORKS ACTIONS
NEW SEC. CABLE ONLY (DUCT)
RRM — REMOVE / PROTECT / RE-FIX
EXISTING ASSETS (AS-BUILT)
EXISTING AGL ASSET — see asset key
AGL FEED MANHOLE / HANDHOLE
AREAS & LINEWORK
MILLING / CUT AREA
AGL WORKS DEMARCATION (GOVERNING)
SECONDARY DUCT CROSSING CUT (INDIC.)
INDICATIVE DUCT — LIGHT TO MH / HH
TAXIWAY CENTRELINE (THROUGH TCC)
TWY EDGE / PAVEMENT (INDIC. 23 m)
ASSET KEY (AS-BUILT LABEL PREFIX)
TCCECH — Taxiway centreline light ×9
HH — Handhole ×2
P2 — Civil pit (transformer handhole) ×1
RRM — Runway guard light / RRM ×5
X_CV_STH_PITS — Civil pit / transformer HH ×1

## Slide 4
SHOP DRAWING — ELECTRICAL / AGL SCOPE (FIELD-GOVERNED) · TAXIWAY E (E4–E6) — LOCATION 3 · DWG NO AUH-SK-AGL-TWYE-001-1003 REV P07
UTM 40N (EPSG:32640) — AS-BUILT POSITIONS · DO NOT SCALE FROM DRAWING
AGL WORKS DEMARCATION — PER FIELD-VERIFIED AFFECTED ASSETS (614.4 m²)
RRM.283
P4.036.399
TCCECH.04.005
TCCECH.04.004
RRM.547
RRM.548
RRM.558
RRM.559
RRM.655
RRM.669
HH.E.144
TCCECH.03.006
TCCECH.03.004
TCCECH.03.005
TCCECH.05.034
TCCECH.05.033
TCCECH.06.035
TCCECH.06.036
EL.EBASE.13328
EL.EBASE.13329
EL.EBASE.13330
EL.EBASE.13331
TCC102.01.052
TCC102.02.050
TCCECH.03.001
TCCECH.05.016
TCCECH.05.017
TCCECH.06.019
TCCECH.06.017
TCCECH.06.018
TCCECH.04.001
TCCECH.05.018
P4.037
P4.039
HH.E.057
HH.E.061
HH.E.060
HH.E4.010
HH.E.058
HH.E.059
P4.041
MH.E.015
MH.E.023
SGC102.02.015
SGC102.02.014
SBC102-01/038
SBC102-01/039
SBC102-02/035
SBC102-02/036
SBC102-01/040
SBC102-01/041
SBC102-02/037
SBC102-02/038
TCCECH-03/002
TCCECH-04/002
TCCECH-03/003
TCCECH-04/003
RRM.557
RRM.670
LOCATION 3 — 1003 · REV P07 (ISSUED)
SCOPE PER FIELD SHEET Second_milling_area rev _1 (12 No. LIGHTS LISTED) — FIELD CONDITION GOVERNS (supersedes the earlier no-works revision)
Sheet A3 (420 x 297 mm) · NOT TO SCALE — approx. 1:465 as plotted · UTM 40N · Issued 28.07.2026 · Rev P07 30.07.2026 · Prepared: Mohammed, AGL Team Leader — ADB SAFEGATE · Approved: Ragesh Menon, AGL Manager
SCOPE / QUANTITIES (PER FIELD VERIFICATION)
SHALLOW BASE AFFECTED — NO CORING; DUMMY PLATE + CABLE (SAWCUT): 4 No.
• SBC102-01/038, 01/039, 02/035, 02/036 (EP7 STOP BAR)
NEW SECONDARY CABLE ONLY (VIA DUCT): 8 No.
• SBC102-01/040, 01/041, 02/037, 02/038, TCCECH-03/002, 04/002, 03/003, 04/003
FIELD SHEET TOTAL: 12 No. — all 12 secondary-cable affected; 4 shallow-base affected (YES)
RRM.557 (0.07 m — treat as within works) & RRM.670: REMOVE / PROTECT / RE-FIX
ISOLATE CIRCUITS: SBC102.01/.02, TCCECH.03/.04
DUMMY PLATES: 4 No. — NO CORING HERE; BASES RETAINED & BLANKED (BLACK SQUARE)
GENERAL NOTES
1. All asset positions as-built (asset survey assets_20260726120533.xlsx, UTM 40N / EPSG:32640).
2. AGL works demarcation (red) drawn around field-verified affected assets (+2.0 m) — field condition governs.
3. Secondary cables: no joints — full manhole-to-light replacement. Confirm routes vs AGL duct-layout CAD (Rev C) before works.
4. Isolate, lock out & prove dead all listed circuits at CCR under permit before any cutting, coring or excavation.
5. Reinstatement setting-out by civil survey from as-built E/N, checked against adjacent undisturbed fittings before coring.
6. Rev P07: every asset on this sheet re-marked directly from field sheet Second_milling_area rev _1 (1st table) — outer ring from the Secondary-cable / Shallow-base columns, inner disc from Duct / Sawcut. Assets not listed on the field sheet are shown grey with no action assumed.
7. Asset key: label prefix to as-built class, from the AGL asset survey checked against the AGL duct-layout CAD. Civil items (HH / MH / pits / RRM) plot about 2.1 m from the surveyed insertion point — set out from survey, not from this sheet. A pit prefix can cover more than one civil class (manhole, transformer handhole, earthing); confirm the individual pit before works.
WORKS ACTIONS
BASE RETAINED + DUMMY PLATE (SAWCUT)
NEW SEC. CABLE ONLY (DUCT)
RRM — REMOVE / PROTECT / RE-FIX
FITTING LIFTED + OPENING PROTECTED
EXISTING ASSETS (AS-BUILT)
EXISTING AGL ASSET — see asset key
AGL FEED MANHOLE / HANDHOLE
AREAS & LINEWORK
MILLING / CUT AREA
AGL WORKS DEMARCATION (GOVERNING)
SECONDARY DUCT CROSSING CUT (INDIC.)
INDICATIVE DUCT — LIGHT TO MH / HH
TAXIWAY CENTRELINE (THROUGH TCC)
STOP BAR (THROUGH SBC)
TWY EDGE / PAVEMENT (INDIC. 23 m)
ASSET KEY (AS-BUILT LABEL PREFIX)
EL — Existing light base (EBASE) ×4
SBC102 — Stop bar light ×8
SGC102 — Sign foundation ×2
TCC102 — Taxiway centreline light ×2
TCCECH — Taxiway centreline light ×21
HH — Handhole ×7
MH — Manhole ×2
P4 — Civil pit (manhole / transformer HH) ×4
RRM — Runway guard light / RRM ×9

## Slide 5
CONSOLIDATED FIELD-GOVERNED SCOPE — TWY E (E4–E6)
Loc | Asset | Works Action | Route | Remarks
LOC-01 | SBC102-02/024 | CORE OUT + NEW CABLE | Duct | Core out shallow base + full cable replacement
LOC-01 | SBC102-01/027 | CORE OUT + NEW CABLE | Duct | Core out shallow base + full cable replacement
LOC-01 | SBC102-02/025 | CORE OUT + NEW CABLE | Duct | Core out shallow base + full cable replacement
LOC-01 | SBC102-01/028 | CORE OUT + NEW CABLE | Duct | Core out shallow base + full cable replacement
LOC-01 | SBC102-02/026 | CORE OUT + NEW CABLE | Duct | Core out shallow base + full cable replacement
LOC-01 | SBC102-01/029 | CORE OUT + NEW CABLE | Duct | Core out shallow base + full cable replacement
LOC-01 | TCCECH-04/034 | CORE OUT + NEW CABLE | Sawcut | Core out shallow base + full cable replacement
LOC-01 | TCCECH-03/036 | CORE OUT + NEW CABLE | Sawcut | Core out shallow base + full cable replacement
LOC-01 | TCCECH-04/035 | CORE OUT + NEW CABLE | Sawcut | Core out shallow base + full cable replacement
LOC-01 | TCCECH-03/037 | CORE OUT + NEW CABLE | Sawcut | Core out shallow base + full cable replacement
LOC-01 | TCCECH-04/036 | CORE OUT + NEW CABLE | Sawcut | Core out shallow base + full cable replacement
LOC-01 | SBC102-02/027 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-01 | TCCECH-03/035 | NEW CABLE ONLY | Sawcut | Field sheet: sec. cable YES / shallow base NO — no coring, no dummy plate; full cable replacement via sawcut
LOC-01 | TCCECH-03/018 | NEW CABLE ONLY | Sawcut | Field sheet: sec. cable YES / shallow base NO — no coring, no dummy plate; full cable replacement via sawcut
LOC-01 | TCC103-11/021 | NOT ON FIELD SHEET — CONFIRM | — | Not listed on Document_3. Secondary route appears to cross the cut (2.0 m in cut) — confirm scope before works; no action assumed
LOC-01 | TCC103-11/126 | NOT ON FIELD SHEET — CONFIRM | — | Not listed on Document_3. Secondary route appears to cross the cut (2.0 m in cut) — confirm scope before works; no action assumed
LOC-01 | TCC103-12/021 | NOT ON FIELD SHEET — CONFIRM | — | Not listed on Document_3. Secondary route appears to cross the cut (2.0 m in cut) — confirm scope before works; no action assumed
LOC-01 | TCC103-12/022 | NOT ON FIELD SHEET — CONFIRM | — | Not listed on Document_3. Secondary route appears to cross the cut (7.8 m in cut) — confirm scope before works; no action assumed
LOC-01 | SBC102-01/026 | NOT AFFECTED |  | 
LOC-02 | TCCECH-03/007 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-02 | TCCECH-04/007 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-02 | TCCECH-03/008 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-02 | TCCECH-04/008 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-02 | TCCECH-03/009 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-02 | RRM.555 | RRM REMOVE / PROTECT | — | Remove / protect before sawcut, re-fix after paving
LOC-03 | SBC102-01/038 | DUMMY PLATE + NEW CABLE | Sawcut | Base retained — fitting lifted, dummy plate fitted, full cable replacement
LOC-03 | SBC102-01/039 | DUMMY PLATE + NEW CABLE | Sawcut | Base retained — fitting lifted, dummy plate fitted, full cable replacement
LOC-03 | SBC102-02/035 | DUMMY PLATE + NEW CABLE | Sawcut | Base retained — fitting lifted, dummy plate fitted, full cable replacement
LOC-03 | SBC102-02/036 | DUMMY PLATE + NEW CABLE | Sawcut | Base retained — fitting lifted, dummy plate fitted, full cable replacement
LOC-03 | SBC102-01/040 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-03 | SBC102-01/041 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-03 | SBC102-02/037 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-03 | SBC102-02/038 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-03 | TCCECH-03/002 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-03 | TCCECH-04/002 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-03 | TCCECH-03/003 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-03 | TCCECH-04/003 | NEW CABLE ONLY | Duct | Full manhole-to-light cable replacement
LOC-03 | RRM.557 | RRM REMOVE / PROTECT | — | Remove / protect before sawcut, re-fix after paving
LOC-03 | RRM.670 | RRM REMOVE / PROTECT | — | Remove / protect before sawcut, re-fix after paving

## Slide 6
CONSOLIDATED SCOPE TOTALS — TWY E (E4–E6)
1,887.3 m²
Total demarcation area
11
Core-outs (LOC-01 only)
8
Dummy plates
4 (LOC-03) + 4 TCC103 unconfirmed
31
Secondary cable runs
per field sheets; +4 TCC103
3
RRMs
1
Field-verified not affected
NOT ON FIELD SHEET — TCC103 (4 No.)
DEMARCATION AREA BY LOCATION
LOC-01 (sheet 1001) — 572.6 m² LOC-02 (sheet 1002) — 700.3 m² LOC-03 (sheet 1003) — 614.4 m² Total — 1,887.3 m²
11
Saw-cut route runs
LOC-01: 7 • LOC-03: 4 • +4 TCC103 not on field sheet • 13.8 m of secondary cable inside the cut
20
Duct route runs (secondary cable)
LOC-01: 7 • LOC-02: 5 • LOC-03: 8 • existing duct, pulled manhole-to-light
TCC103-11/021 — not listed; cable may cross cut (2.0 m) — confirm
TCC103-11/126 — not listed; cable may cross cut (2.0 m) — confirm
TCC103-12/021 — not listed; cable may cross cut (2.0 m) — confirm
TCC103-12/022 — not listed; cable may cross cut (7.8 m) — confirm